## Slide 1: Computer networks
A computer network is a group of two or more computer systems linked together.
The connections between computers in a network are usually made using physical wires or cables
Generally, networks are distinguished based on their geographical span.
E.g A network can be as small as distance between your mobile phone and its Bluetooth headphone and as large as the internet itself, covering the whole geographical world.

## Slide 2: ADVANTAGES OF NETWORKS
Speed: sharing and transferring files within networks are very rapid. Thus saving time, while maintaining the integrity of the file.
Cost: Individually licensed copies of many popular software programs can be costly. Shared programs on a network allows for easier upgrading of the program on the single file server, instead of upgrading individual workstations.
Security: sensitive files and programs on a network are password protected .
Centralized software management: software can be loaded on one computer (the file server) eliminating the need to spend time and energy installing updates and tracking files on independent computers throughout the building.
Resource sharing
Flexible access: access their files from computers throughout the firm.
Workgroup computing: workgroup software allows many users to work on a document or project concurrently.

## Slide 3: Importance of Computer Networks
Facilitating communications: Using a network, people can communicate efficiently and easily via email, instant massaging, chat rooms, telephone, etc.
Sharing hardware: In a networked environment, each computer on a network may access and use hardware resources on the network, such as printing a document on a shared network printer.
Sharing files, data and information: In a networked environment, authorized users may access data and information stored on other computers on the network.
Sharing software: Users connected to a network may run application programs on remote computers

## Slide 4: NETWORK CRITERIA
A good network must meet the following 3 criteria's:
Performance
Performance can be measured using:
  Transit time- time taken to travel a message from one device to another
  Response time – time elapsed between enquiry and response
  The network performance depends on the following factors:
        Number of users
        Type of transmission medium
        Efficiency of software
        Good performance can be obtained by achieving higher throughput and smaller delay times.

## Slide 5
Reliability
Reliability is measured by:
  Frequency of network failure
  Time taken to recover from a network failure
  Network’s robustness in a disaster.
  More the failures are, less is the network’s reliability.
Security
Security refers to the protection of data from the unauthorized access or damage.
It also involves implementing policies for recovery from data-losses.

## Slide 6
STEPS REQUIRED TO DESIGN A GOOD NETWORK ARE:
Step 1. Verify the business goals and technical requirements.
Step 2. Determine the features and functions required to meet the needs identified in Step 1.
Step 3. Perform a network-readiness assessment.
Step 4. Create a solution and site acceptance test plan.
Step 5. Create a project plan.

## Slide 7
FUNDAMENTAL DESIGN GOALS
■ Scalability: Scalable network designs can grow to include new user groups and remote sites and can support new applications without impacting the level of service delivered to existing users.
■ Availability: A network designed for availability is one that delivers consistent, reliable performance, 24 hours a day, 7 days a week. In addition, the failure of a single link or piece of equipment should not significantly impact network performance.
■ Security: Security is a feature that must be designed into the network, not added on after the network is complete. Planning the location of security devices, filters, and firewall features is critical to safeguarding network resources.
■ Manageability: No matter how good the initial network design is, the available network staff must be able to manage and support the network. A network that is too complex or difficult to maintain cannot function effectively and efficiently.

## Slide 8
FACTORS IMPACTING THE ENTIRE NETWORK
Network requirements that impact the entire network include the following:
■ Adding new network applications and making major changes to existing applications, such as database or Domain Name System (DNS) structure changes
■ Improving the efficiency of network addressing or routing protocol changes
■ Integrating new security measures
■ Adding new network services, such as voice traffic, content networking, and storage networking
■ Relocating servers to a data center server farm
FACTORS IMPACTING A PORTION OF THE NETWORK
Requirements that may only affect a portion of the network include the following:
■ Improving Internet connectivity and adding bandwidth
■ Updating access layer LAN cabling
■ Providing redundancy for key services
■ Supporting wireless access in defined areas
■ Upgrading WAN bandwidth

## Slide 9: Types of computer networks Based on Geographical Span
Personal Area Network (PAN)
Is smallest network which is very personal to a user. This may include Bluetooth enabled devices or infra-red enabled devices. PAN has connectivity range up to 10 meters.
PAN may include wireless computer keyboard and mouse, Bluetooth enabled headphones, wireless printers, and TV remotes.

## Slide 10
Local Area Network (LAN)
A computer network spanned inside a building and operated under single administrative system.
Usually, LAN covers an organization offices.
LAN provides a useful way of sharing the resources between end users. The resources such as printers, file servers, scanners, and internet are easily sharable among computers.
LANs are capable of transmitting data at very fast rates, much faster than data can be transmitted over a telephone line; but the distances are limited, and there is also a limit on the number of computers that can be attached to a single LAN.

## Slide 11: TYPES OF LAN
Token Ring : In the token ring a token ring passes over a physical ring. Token ring is defined by IEEE 802.5 standard. In token ring, there is a station and a special frame called token. A station in token ring can transmit data frame if it contains a token. After the successful transmission of data frame token are pointed(issued). Token ring is a Star shaped topology and handles priority in which some nodes may give priority to the token.

## Slide 12
2. Ethernet : IEEE 802.3 defines the Ethernet. It uses CSMA/CD mechanism. It means that if many stations exist at the same time to talk, all stations will be closed. To resume them, wait for a random time. Unlike token ring it doesn’t employ any priorities. And it is less costly than token ring network.

## Slide 13
3. Token Bus
This is also a type of Local Area Network developed by IBM.
Token Bus standard uses copper cables which are coaxial for connecting multiple devices to the main large computers or workstations. The coaxial cable acts as the common communication bus.
In this protocol, also a token is created by this protocol to manage access for communication.
Any computer that holds the token can transfer the data. The token is released when the station completes its data transmission or when a higher priority device needs to transmit (such as the mainframe).
Due to the token freeing mechanism, there is no collision, i.e. two or more devices can easily transmit information on the bus at the same time, and the transmitted data is also saved from being destroying.

## Slide 14
4. Fiber Distributed Data Interface (FDDI)
It is a LAN standard used for data transmission via optical media.
Used for long-distance networks. Uses optical fiber and copper cable.
It provides communication with fiber optic cables up to 200 kilometers at a speed of 100 Mbps. FDDI has two token rings, primary and secondary communication rings. One ring is for backup in the case when the primary one fails.
The primary ring works, and the second one remains free and is available for backup. It is extended to FDDI-2 for long-distance voice and multimedia communication. It is used for huge and fast data transfer, such as in voice and video conferences, online lectures, news, etc.
It was displaced by fast Ethernet, which is cheaper and has a faster data transfer rate. It is used in a large geographical scenario with thousands of end-users.

## Slide 15: ADVANTAGES OF LAN
Files can be stored on a central computer (the file server) allowing data to be shared throughout an organization.
Files can be backed up more easily when they are all on a central fileserver rather than when they are scattered across a number of independent workstations.
Networks also allow security to be established, ensuring that the network users may only have access to certain files and applications.
Software and resources can be centrally managed.
Network versions of software often allow for their speedy installation on workstations from the file server.
Expensive devices such as laser printers or scanners can be shared.
Users can access their files from any workstation

## Slide 16: DISADVANTAGES OF LAN
Power - a good LAN is required to be on all the times.
Security - each computer and device become another point of entry for undesirables.
Upkeep - when things go wrong or the software gets updated.
Frustration if having a problem setting up.
A lot of times a network shares one Internet connection - if all computers are running at once, there can be reduced speed for each.
Area covered is limited.

## Slide 17
Metropolitan Area Network (MAN)
A data network designed for a town or city.
In terms of geographic breadth, MANs are larger than local-area networks (LANs), but smaller than wide-area networks (WANs). MANs are usually characterized by very high-speed connections using fiber optical cable or other digital media.

## Slide 18
Wide-Area Network - WAN
A computer network that spans a relatively large geographical area. Typically, a WAN consists of two or more local-area networks (LANs).
Computers connected to a wide-area network are often connected through public networks, such as the telephone system. They can also be connected through leased lines or satellites. The largest WAN in existence is the Internet.
Campus network

## Slide 20: BASIC TERMINOLOGIES
Topology : The geometric arrangement of devices on the network. For example, devices can be arranged in a ring or in a straight line.
Protocols : The rules and encoding specifications for sending data. The protocols also determine whether the network uses a peer-to-peer or client/server architecture.
Media : Devices can be connected by twisted-pair wire, coaxial cables, or fiber optic cables. Some networks do without connecting media altogether, communicating instead via radio waves.

## Slide 21: CATEGORIES OF NETWORK TOPOLOGIES
1. Physical Topology : It reflects physical layout of devices and cables to a form a connected network. It is concerned with essentials of network ignoring minute details like transfer of data and device type. The pattern of arrangement of nodes (computers) and network cables depends on ease of installation and setup of the network. It affects cost and bandwidth capacity based on solution of devices. It takes into account placement of nodes and distance between them. Devices can be arranged to form a ring (Ring Topology) or linearly connected in a line called Bus Topology.
2. Logical Topology : Logical Topology reflects arrangement of devices and their communication. It is the transmission of data over physical topology. It is independent of physical topology, irrespective of arrangements of nodes. It is concerned with intricate details of network like type of devices (switches, routers) chosen and their quality, which affect rate and speed of data packets delivery. The logical topology ensures optimal flow control that can be regulated within network. The data can either flow in a linear pattern called Broadcast/Logical bus or in form of a Sequential/ Logical ring/.

## Slide 22
TYPES OF NETWORKS BASED ON LOGICAL TOPOLOGY
Hierarchical Network Design
In networking, a hierarchical design is used to group devices into multiple networks. The networks are organized in a layered approach.
The hierarchical design model has three basic layers:
■ Core layer: Connects distribution layer devices
■ Distribution layer: Interconnects the smaller local networks
■ Access layer: Provides connectivity for network hosts and end devices
Hierarchical networks have advantages over flat network designs.
The benefit of dividing a flat network into smaller, more manageable hierarchical blocks is that local traffic remains local. Only traffic destined for other networks is moved to a higher layer.
Layer 2 devices in a flat network provide little opportunity to control broadcasts or to filter undesirable traffic

## Slide 23
Flat Network
All devices are connected to one connection
As more devices and applications are added to a flat network, response times degrade until the network becomes unusable
The Cisco Enterprise Architectures --can be used to further divide the three-layer hierarchical design into modular areas. The modules represent areas that have different physical or logical connectivity. They designate where different functions occur in the network. This modularity enables flexibility in network design. It facilitates implementation and troubleshooting. Three areas of focus in modular network design are as follows:
■ Enterprise campus: This area contains the network elements required for independent operation within a single campus or branch location. This is where the building access, building distribution, and campus core are located.
■ Server farm: A component of the enterprise campus, the data center server farm protects the server resources and provides redundant, reliable high-speed connectivity.
■ Enterprise edge: As traffic comes into the campus network, this area filters traffic from the external resources and routes it into the enterprise network. It contains all the elements required for efficient and secure communication between the enterprise campus and remote locations, remote users, and the Internet.

## Slide 24: LAN Transmission Methods
LAN data transmissions fall into three classifications: unicast, multicast, and broadcast. In each type of transmission, a single packet is sent to one or more nodes.
In a unicast transmission, a single packet is sent from the source to a destination on a network.
A multicast transmission consists of a single data packet that is copied and sent to a specific subset of nodes on the network.
A broadcast transmission consists of a single data packet that is copied and sent to all nodes on the network.

## Slide 25
TYPES OF PHYSICAL NETWORK TOPOLOGIES:
Star Topology.
Bus Topology.
Ring Topology.
Mesh Topology.
Tree Topology.
Hybrid Topology.

## Slide 26
Bus topology
It is also known as linear bus.
Consists of a single cable that runs to every work-station. In other words, all the nodes (computers and servers) are connected to the single/central cable (called bus), by the help of interface connectors.
This central cable is the back bone of the network and every workstation communicates with the other device through this bus.
A data from the source is broadcasted to all devices connected to the bus.
Only the intended-receiver, whose physical-address matches, accepts the data.
Devices are connected to the bus by drop-lines and taps.
A drop line is a connection running between the device and the bus.
A tap is a connector that links to the bus.
The data is sent in only one direction and as soon as it reaches the extreme end, the terminator removes the data from the line.
Used in Ethernet systems.

## Slide 27
Advantages of Bus topology
Easy installation
Cable required is the least compared to mesh/star topologies
Redundancy is limited
Costs less (compared to mesh/star topologies)
Mostly used in small networks, good for LAN.
Disadvantages of Bus topology
Difficult to detect and troubleshoot fault
Signal reflection at the taps can cause degradation in quality
A fault / break in the cable stops all transmission
There is a limit on:
  Cable length
  Number of nodes that can be connected.
Security is very low because all the devices receive the data sent from the source.

## Slide 28
Drop line
Tap
Bus Topology

## Slide 29
Ring topology
All devices are connected to one another in the shape of a closed loop (ring), so that each device is connected directly to two other devices, one on either side of it.
When one device tries to communicate or send message to a device which is not adjacent to it, the data travels in one direction around the network till the destination is reached.
Sending and receiving of data takes place by the help of token.
Each device has a repeater.
A repeater
  Receives a signal on transmission medium and
  Regenerates and passes the signal to the next device
Failure of any host results in failure of the whole ring. Thus, every connection in the ring is a point of failure.

## Slide 30
Advantages of Ring topology
Easy to install and reconfigure: to add/delete a device, requires changing only 2 connections.
Fault isolation is simplified: if one device does not receive a signal within a specified period, it can issue an alarm. The alarm alerts the network operator the problem and its location
Congestion is reduced: because all the traffic flows in only one direction.
Disadvantages of Ring topology
Unidirectional traffic
A fault in the ring/device stops all transmission
There’s a limit on:
  Cable length
  Number of nodes that can be connected
Slower: each data must pass through all the devices between source and destination.

## Slide 31
Ring topology

## Slide 32
Star topology
All the devices are connected to a central controller called a hub.
That is, there exists a dedicated point-to-point connection between a device and a hub.
The devices are not directly linked to one another. Thus, there’s no direct traffic between devices.
The hub acts as a junction:
  If a device-1 wants to send data to device-2,
    The device sends the data to the hub,
      Then, the hub relays the data to the device-2
The central device can be any of the following:
  Layer-1 device such as hub or repeater
  Layer-2 device such as switch or bridge
  Layer-3 device such as router or gateway

## Slide 33
Start topology

## Slide 34
Advantages of Star topology
Less expensive: each device needs only one link and one I/O port to connect it to any devices.
Easy to install and reconfigure: nodes can be added/ removed without affecting the network.
Robustness: if one link fails, it does not affect the entire system.
Easy to detect and troubleshoot fault.
Centralized management: the hub manages and controls the whole network.
Disadvantages of star topology
Single point of failure: if the hub goes down, the whole network is dead
Cable length required is more compared to bus/ring topologies
Number of nodes in a network depends on capacity of hub

## Slide 35
Mesh Topology
It is a point-to-point connection to other nodes or devices.
Every device not only sends its only data but also relays data from other nodes.
Every device must have (n-1) I/O ports to be connected to the other (n-1) devices.
Mesh has n(n-1)/2 physical channels to link n devices.
There are two techniques to transmit data over the Mesh topology, they are :
Routing - In routing, the nodes have a routing logic, as per the network requirements. Like routing logic to direct the data to reach the destination using the shortest distance. Or, routing logic which has information about the broken links, and it avoids those node etc. We can even have routing logic, to re-configure the failed nodes.
Flooding - In flooding, the same data is transmitted to all the network nodes, hence no routing logic is required. The network is robust, and the its very unlikely to lose the data. But it leads to unwanted load over the network.

## Slide 36
Mesh Topology
Types of Mesh Topology
Partial Mesh Topology : In this topology some of the systems are connected in the same fashion as mesh topology but some devices are only connected to two or three devices.
Full Mesh Topology : Each and every nodes or devices are connected to each other.

## Slide 37
Advantages of mesh topology
Congestion reduced: each connection can carry its own data load.
Robustness: if one link fails, it does not affect the entire system
Security: when data travels on a dedicated line, only the intended receiver can see the data.
Easy fault identification and fault isolation: traffic can be re-routed to avoid problematic links
Disadvantages of mesh topology
Difficult to install and reconfigure
Bulk of wiring occupy more space than available space
Very expensive: as there are many redundant connections
Not mostly used in wired computer networks. Commonly used in wireless networks
High redundancy of network connection.

## Slide 38
TREE TOPOLOGY - It has a root node and all other nodes are connected to it forming a hierarchy. It is also called hierarchical topology. It should at least have three levels to the hierarchy.

## Slide 39
Hybrid Topologies
These topologies can also be mixed. For example, a bus-star network consists of a high-bandwidth bus, called the backbone, which connects a collection of slower-bandwidth star segments.

## Slide 40: LAN Administration
From an administrator’s point of view, a network can be private network which belongs a single autonomous system and cannot be accessed outside its physical or logical domain.
A network can be public, which is accessed by all.